## Slide 1
Introduction to classical
deconvolution
Patrick La Riviere, Ph.D.
Associate Professor,
Radiology and Medical Physics
The University of Chicago
NCBM Deep Learning workshop MBL 2019

## Slide 2
Overview

## Slide 3
Imaging workflow
imaging hardware & methods development
physicists and engineers
Shroff, Oldenbourg, Shribak
computational imaging methods: tomography, deconvolution
computational scientists (inverse problems)
La Riviere
sample prep molecular & chemical probes
biologists, chemists and physicists
Selvin, Tani
image analysis: segmentation, particle tracking
computational scientists (image processing)
Danuser
biological question
biologists
Gladfelter, Waterman, Colon-Ramos, etc
?

## Slide 4: Computing on images
Results of connectivity analysis for retinal cells from synchrotron microCT. From Gordon Kindlmann (UChicago Computer Science).
Extracting information from images that is difficult or tedious for humans to do.
Nuclear segmentation and wireframe modeling of C. Elegans (Hari Shroff)

## Slide 5: Computing to form images
Some imaging systems are inherently a combination of measurements and computation.
You need algorithms to solve inverse problems
to get the desired image.
You need mathematical algorithms implemented on computers to get this:
A light field microscope measures this:
You need mathematical algorithms implemented on computers to get this:
A CT scanner measures this:

## Slide 6: Computing to form images: deblurring/deconvolution
Naïve
Decon.
Better
Decon.

## Slide 7
Setting up the
deconvolution problem

## Slide 8: Imaging as a mapping between functions
An imaging system maps from 2D or 3D object function to a 2D or 3D image or image stack.
Notes: Famous image from Rene Magritte. If it’s not a pipe, what is it? It’s an IMAGE of a pipe. Not the object itself but a representation of the object.
It’s made of paint and brushstrokes instead of wood and tobacco and subject to the distortion and interpretation of the artist’s perspective.
So we must remember that scientific images are, similarly, representations of their subjects. As representations they are distorted by the image capture device (telescope, microscope, camera, etc). The image of a point is not a point, it is a pattern of light called a point spread function (PSF).

## Slide 9: Most imaging systems are linear
Linearity exists if superimposition holds:
The image created from a weighted sum of inputs equals the same weighted sum of the corresponding individual images.
Notes: Famous image from Rene Magritte. If it’s not a pipe, what is it? It’s an IMAGE of a pipe. Not the object itself but a representation of the object.
It’s made of paint and brushstrokes instead of wood and tobacco and subject to the distortion and interpretation of the artist’s perspective.
So we must remember that scientific images are, similarly, representations of their subjects. As representations they are distorted by the image capture device (telescope, microscope, camera, etc). The image of a point is not a point, it is a pattern of light called a point spread function (PSF).

## Slide 10: Most imaging systems are shift-invariant
Shifting the input just shifts the output
Notes: Famous image from Rene Magritte. If it’s not a pipe, what is it? It’s an IMAGE of a pipe. Not the object itself but a representation of the object.
It’s made of paint and brushstrokes instead of wood and tobacco and subject to the distortion and interpretation of the artist’s perspective.
So we must remember that scientific images are, similarly, representations of their subjects. As representations they are distorted by the image capture device (telescope, microscope, camera, etc). The image of a point is not a point, it is a pattern of light called a point spread function (PSF).

## Slide 11: A linear, shift-invariant system can be characterized by a point spread function (PSF)
Intensity
For a linear, shift-invariant system, the response of the system to an idealized point allows us to calculate the response to any general object!
Notes: If you were to draw a line across a PSF and plot the signal intensity as a function of distance, you would plot a representation of the Airy pattern.
The bright, central portion of the Airy pattern is called the Airy disk.
Measuring across the Airy disk at a point halfway to the maximum intensity gives the full width at half max (FWHM). The smaller your FWHM, the better the resolution of your imaging system.

## Slide 12: Typical microscopy PSF, aka Airy pattern
The better the spatial resolution of your system, the smaller the PSF/ Airy pattern.
Measurement of the full width at half maximum (FWHM) intensity is one way to determine resolution.
Image credit: Bolte and Corderlieres (2006) J. Microscopy v. 224 pt3, pg. 214
Distance
Intensity
Slide adapted from Christine Labno, UChicago
Notes: If you were to draw a line across a PSF and plot the signal intensity as a function of distance, you would plot a representation of the Airy pattern.
The bright, central portion of the Airy pattern is called the Airy disk.
Measuring across the Airy disk at a point halfway to the maximum intensity gives the full width at half max (FWHM). The smaller your FWHM, the better the resolution of your imaging system.

## Slide 13: From Point Spread Functions to Transfer Functions: Thinking in frequency space
Starring Goofy
Special guest star:
the Airy Fairy
Notes: λ is the wavelength of light used for imaging, typically between 400 and 800nm
NA is the numerical aperture of the objective, typically between 0.1 and 1.45. NA is a measure of resolving power of the microscope and also a measure of light gathering capability.
For practical purposes, the higher the NA, the better the resolution and the greater the light gathering power.

## Slide 14: Thinking in frequency space
Any well-behaved function can be expressed as a weighted sum over sinusoids.
We characterize each sinusoid by a frequency.
Higher frequency means wiggles faster.
Not surprisingly, a high-resolution imaging system is able to capture higher frequencies.
NOTE: We are NOT talking about different wavelengths of light here.
Notes: λ is the wavelength of light used for imaging, typically between 400 and 800nm
NA is the numerical aperture of the objective, typically between 0.1 and 1.45. NA is a measure of resolving power of the microscope and also a measure of light gathering capability.
For practical purposes, the higher the NA, the better the resolution and the greater the light gathering power.

## Slide 15: The Fourier transform
Taking a function apart into its constituent sinusoids is called a Fourier transform.
Notes: λ is the wavelength of light used for imaging, typically between 400 and 800nm
NA is the numerical aperture of the objective, typically between 0.1 and 1.45. NA is a measure of resolving power of the microscope and also a measure of light gathering capability.
For practical purposes, the higher the NA, the better the resolution and the greater the light gathering power.

## Slide 16: Fourier transform pairs
Notes: λ is the wavelength of light used for imaging, typically between 400 and 800nm
NA is the numerical aperture of the objective, typically between 0.1 and 1.45. NA is a measure of resolving power of the microscope and also a measure of light gathering capability.
For practical purposes, the higher the NA, the better the resolution and the greater the light gathering power.

## Slide 17: Wider in one domain means narrower in the other

## Slide 18: Thinking in 2D frequency space
Notes: λ is the wavelength of light used for imaging, typically between 400 and 800nm
NA is the numerical aperture of the objective, typically between 0.1 and 1.45. NA is a measure of resolving power of the microscope and also a measure of light gathering capability.
For practical purposes, the higher the NA, the better the resolution and the greater the light gathering power.

## Slide 19: Thinking in 2D frequency space
2d sinusoids
Their Fourier transforms
Notes: λ is the wavelength of light used for imaging, typically between 400 and 800nm
NA is the numerical aperture of the objective, typically between 0.1 and 1.45. NA is a measure of resolving power of the microscope and also a measure of light gathering capability.
For practical purposes, the higher the NA, the better the resolution and the greater the light gathering power.

## Slide 20
from http://www.cs.unm.edu/~brayer/vision/fourier.html
original
image

## Slide 21
from http://www.cs.unm.edu/~brayer/vision/fourier.html
original
image
Fourier
transform

## Slide 22
from http://www.cs.unm.edu/~brayer/vision/fourier.html
original
image
Suppress
high
horizontal
frequencies
Fourier
transform

## Slide 23
from http://www.cs.unm.edu/~brayer/vision/fourier.html
original
image
x-blurred
image
Fourier
transform
Suppress
high
horizontal
frequencies

## Slide 24
original
image

## Slide 25
original
image
Fourier
transform

## Slide 26
original
image
Fourier
transform
truncated
Fourier
transform

## Slide 27
original
image
Fourier
transform
reconstructed
“inverse FT”
image
truncated
Fourier
transform

## Slide 28: A lens as a Fourier optic
40x NA 1.15 water
350ms exposure
40x NA 0.6 dry
350ms exposure
40x NA 1.35 oil
350ms exposure
Input pattern
Lens decomposes spatial frequencies. Highest ones get truncated by lens aperture.
Output pattern
Notes: Use the highest NA objective available. Increasing NA increases resolution / sharpness and light gathering ability. With higher NA generally comes some form of immersion, and that helps with light gathering ability as well.

## Slide 29: Convolution-multiplication theorem
Multiplying in the Fourier domain by a function is the same as convolving in the spatial domain with the FT of that function.
Since a lens effectively multiplies the FT of the function by a circle, it is like convolving in spatial domain with the FT of a circle.
Notes: Use the highest NA objective available. Increasing NA increases resolution / sharpness and light gathering ability. With higher NA generally comes some form of immersion, and that helps with light gathering ability as well.

## Slide 30: What is the FT of a circle? A function whose square is the Airy pattern! (Square because we measure intensities not amplitudes and fluorescence is incoherent).
Notes: Use the highest NA objective available. Increasing NA increases resolution / sharpness and light gathering ability. With higher NA generally comes some form of immersion, and that helps with light gathering ability as well.

## Slide 31: What Determines the Size of the Airy Disk?
Image credit: Olympus Microscopy Resource Center
Resolution (xy) = d = λ / 2NA
Resolution (z) = d = 2λ /NA²
Where λ is the wavelength of light used for imaging
NA is the numerical aperture of the objective
These equations were first published by Ernst Abbe in 1873
NA = 0.2
NA = 0.8
NA = 1.3
Insert tube lens here
Slide adapted from Christine Labno, UChicago
Notes: λ is the wavelength of light used for imaging, typically between 400 and 800nm
NA is the numerical aperture of the objective, typically between 0.1 and 1.45. NA is a measure of resolving power of the microscope and also a measure of light gathering capability.
For practical purposes, the higher the NA, the better the resolution and the greater the light gathering power.

## Slide 32: Higher Numerical Aperture = Brighter, Sharper Pictures
40x NA 1.15 water
350ms exposure
40x NA 1.35 oil
350ms exposure
Slide adapted from Christine Labno, UChicago
Notes: Use the highest NA objective available. Increasing NA increases resolution / sharpness and light gathering ability. With higher NA generally comes some form of immersion, and that helps with light gathering ability as well.

## Slide 33: Optical transfer functions (OTF)
40x NA 0.6 dry
350ms exposure
40x NA 1.35 oil
350ms exposure
We can use the convolution multiplication theorem to move our imaging equation into frequency space.
The Fourier transform of a PSF is called an optical transfer function OTF.
Notes: Use the highest NA objective available. Increasing NA increases resolution / sharpness and light gathering ability. With higher NA generally comes some form of immersion, and that helps with light gathering ability as well.

## Slide 34: Properties of OTFs
Image of OTF
PSF profile
OTF
profile
Cutoff frequency
Notes: Use confocal microscopy – the confocal pinhole only lets through the light from the Airy Disk, discarding light from the rest of the Airy pattern. This removes blur and reduces the size of the point spread function by approximately 30%. This reduction in PSF size gives better lateral (xy) and axial (z) resolution, allowing us to revise our Rayleigh criterion equation. On the downside, 90% of the light coming from the sample is outside the Airy disk, so your sample appears dimmer without compensation in the form of more excitation light or longer exposure time.

## Slide 35: Properties of OTFs
Tells you how the amplitude of sinusoids of different frequencies are reduced when passed by the imaging system.
Notes: Use confocal microscopy – the confocal pinhole only lets through the light from the Airy Disk, discarding light from the rest of the Airy pattern. This removes blur and reduces the size of the point spread function by approximately 30%. This reduction in PSF size gives better lateral (xy) and axial (z) resolution, allowing us to revise our Rayleigh criterion equation. On the downside, 90% of the light coming from the sample is outside the Airy disk, so your sample appears dimmer without compensation in the form of more excitation light or longer exposure time.

## Slide 36: You want narrow PSFs and wide OTFs
40x NA 0.6 dry
350ms exposure
Notes: Use the highest NA objective available. Increasing NA increases resolution / sharpness and light gathering ability. With higher NA generally comes some form of immersion, and that helps with light gathering ability as well.

## Slide 37: Can’t we solve the OTF equation?
?
Degraded image
Desired image
FT of PSF

## Slide 38: Can’t we solve the OTF equation?
What if this is 0?
Noise gets amplified when OTF is small

## Slide 39: Properties of OTFs
Image of OTF
PSF profile
OTF
profile
Cutoff frequency
Notes: Use confocal microscopy – the confocal pinhole only lets through the light from the Airy Disk, discarding light from the rest of the Airy pattern. This removes blur and reduces the size of the point spread function by approximately 30%. This reduction in PSF size gives better lateral (xy) and axial (z) resolution, allowing us to revise our Rayleigh criterion equation. On the downside, 90% of the light coming from the sample is outside the Airy disk, so your sample appears dimmer without compensation in the form of more excitation light or longer exposure time.

## Slide 40: How to deal with these challenges?
Pseudoinverse: only divide by the OTF when it is not zero. Otherwise set to zero.
Tikhonov regularization: Add a constant to the denominator so you never divide by zero or by a small number.
Gradient-norm regularization: Further modification to the denominator.
All of these are implicitly imposing crude forms of prior information.
Iterative methods with sophisticated priors.
Deep learning with learned priors.
Notes: Use confocal microscopy – the confocal pinhole only lets through the light from the Airy Disk, discarding light from the rest of the Airy pattern. This removes blur and reduces the size of the point spread function by approximately 30%. This reduction in PSF size gives better lateral (xy) and axial (z) resolution, allowing us to revise our Rayleigh criterion equation. On the downside, 90% of the light coming from the sample is outside the Airy disk, so your sample appears dimmer without compensation in the form of more excitation light or longer exposure time.

## Slide 42
Pseudoinverse: only divide by the OTF when it is not zero. Otherwise set to zero. Works well for noiseless data.

## Slide 43
Pseudoinverse: FAILS BADLY FOR NOISY DATA.

## Slide 44
Tikhonov regularization: Add a constant to the denominator so you never divide by zero or by a small number.

## Slide 45
Tikhonov: Better behaved for noisy data. Can control regularization strength.

## Slide 46
Gradient-norm regularization: Further modification to the denominator. (Further suppresses high frequencies.)

## Slide 47
Gradient-norm regularization: Further modification to the denominator. (Further suppresses high frequencies.)

## Slide 48
A deterministic model mapping object to data
Data
Object
System
A noise model for the data
Prior assumptions about object:
f has small roughness R(f)
Objective function:
Find f > 0 maximizing
Algorithm to find maximum of objective function
f(new) =f (old) +U(f(old))
Iterative solutions to inverse problems

## Slide 49
Our goal is to reconstruct an image that is a map of some object property (like fluorophore concentration).
That reconstructed image should agree---in a statistical sense---with the measured data when we act on it with a mathematical model of the imaging system.
That reconstructed image should reflect any prior knowledge or assumptions we wish to impose, either as hard constraints (no negatives allowed!) or soft constraints (encourage smoothness)
In plain English

## Slide 50
  In general, if you try to find the object that agrees well with noisy data, you will get a noisy object.
  We can do better by attempting to enforce some prior knowledge or assumptions about the object.
Sparseness
Limited non-zero pixels in image or its gradient
Non negativity
Pixel values all non-negative
Smoothness
Underlying object more likely to be smooth than rough
Prior assumptions
Prior assumptions about object:
f has small roughness R(f)

## Slide 52: Classical methods vs deep learning
Classical methods generally work well and efficiently when
  You have a good and accurate model of the PSF
  The system is indeed shift invariant in all dimensions, which allows you to use efficient FFTS
  The data quality is high enough that enforcing relatively simplistic priors provides good regularization
Deep learning
  Unknown system model
  Lack of shift invariance
  Very low quality data requiring more subtle learned priors
Deep learning challenges
  You need appropriate pairs of of high and low quality images to train on
  If you do have knowledge of the system PSF, how do you incorporate it?
Notes: Use confocal microscopy – the confocal pinhole only lets through the light from the Airy Disk, discarding light from the rest of the Airy pattern. This removes blur and reduces the size of the point spread function by approximately 30%. This reduction in PSF size gives better lateral (xy) and axial (z) resolution, allowing us to revise our Rayleigh criterion equation. On the downside, 90% of the light coming from the sample is outside the Airy disk, so your sample appears dimmer without compensation in the form of more excitation light or longer exposure time.